## Slide 1: Experiments of 802.15.4 Stack
Data Collection

## Slide 2: Outline
Device & Software
Install
Tools
Practice
  Data Collection
  Advanced
Document Requirements
Grading Policies
Uploading to Ecourse

## Slide 3: Device & Software
Device
FT-6251
  Sensor Development Board x 1
  Antenna x 1
  A/C Adaptor x 1 ; AA Battery Holder x 1
  UART-to-RS232 Serial Converter x 1
USB to RS-232 Cable x1

## Slide 4: Device & Software
Device

## Slide 5: Device & Software
Software
  Windows XP or later (Please don’t use Windows 8)
  RS232 to USB driver
  Code::Blocks
  Cygwin : Jennic Bash Shell
  Jennic Flash Programmer
  Putty

## Slide 6: Preparation
Download hw1.rar
  http://www.cs.ccu.edu.tw/~cih104m/2017_hw1.zip
Jennic Code::Blocks ：IDE install
  Install JN-SW-4026-SDKwithIDE-1v4.8.msi
  Finish
Install Patch
  Install FT-6200-Patch-ba-1v0.exe
  Install Path “where are your IDE”\jennic

## Slide 7: Tools
Jennic Code Block
  Open Jennic Code Block
  Open Lab7.cbp

## Slide 8: Tools
Compile Your Program
  Choose build target

## Slide 9: Tools
Compile Your Program
  Press Build → Rebuild
  View build log
    Status 0: success

## Slide 10: Tools
Jennic Flash Programmer
  Burn our data to FT-6251
  Need install USB to RS232 driver
Step1: open Jennic Flash Programmer
Step2: connect FT-6251to your computer
Step3: Press Browse, choose file which you compiled
  Default path: ..\JN5121_Build\Release

## Slide 11: Tools
Jennic Flash Programmer

## Slide 12: Tools
Jennic Flash Programmer
Step4: power off FT-6251
Step5: power on, FT-6251 come into Program mode
  You will find , only one led is bright
Step6: Press Refresh

## Slide 13: Tools
Jennic Flash Programmer
Step7: press program
Step8: finish
Step9: close flash program and restart FT-6251

## Slide 14: Tools
Output data
  Download putty
  Configure putty

## Slide 15: Practice
Data collection
  End device senses data
  End device transmits data to coordinator
    Data: Short Address、Temperature、 Humidity 、LQI
  Coordinator output information to computer

## Slide 16: Practice
Lab 5 -- HeatTester.c
  vTickTimerISR()
    Observe case E_AHI_DEVICE_TICK_TIMER
    Sense Temperature and Humidity
Lab 7 -- enddevice.c
  vTickTimerISR()
    sense Temperature and Humidity
    Send packets to coordinator
  vWUART_TxData()
    Add Temperature and Humidity to packet
    Array pu8Payload[] stores data

## Slide 17: Practice
Lab 7 -- coord.c
  vProcessIncomingData()
    Store temperature and humidity
    Array au8Sdu[] is array pu8Payload[]
  vDrawUI()
    vDrawUI output the data
    Print temperature and humidity

## Slide 18: Practice
Use putty
Show the data information

## Slide 19: Practice - Advanced
Use LQI(Link Quality Indicator) to calculate the distance between end device and coordinator.
  Observe the relationship between LQI and distance
  LQI is a metric of the current quality of
Write a program to receive serial port data.
  GUI
    Presenting data with any patterns except words in your GUI.
  Allow all of the programing language.

## Slide 20: Practice - Advanced
GUI Example

## Slide 21: Document Requirements
Your document have to include content below:
  Cover (group ID, student ID, name)
  An experimental platform and environment
  The relationship between LQI and distance
  Code and Explanation
  Final Result

## Slide 22: Grading Policies
Demo
  地點:創新大樓lab308
  4/25 (二) 10:00-12:00
  4/26 (三) 10:00-12:00
Grading
  Data Collection 60%
  Advanced 20%
  Report 20%
BUG：-3 point/ BUG
Delayed：-3 point/ Day

## Slide 23: Uploading to Ecourse
Deadline: 2017/04/26
上傳到Ecourse http://ecourse.elearning.ccu.edu.tw/
格式：“組別_hw1.pdf”
同時繳交一份紙本報告給助教

## Slide 24: Question
TA: 趙柏凱
  Email: a65843@gmail.com