## Slide 1: Experiments of Zigbee
Short Address Assignment

## Slide 2: Outline
Device & Software
Preparation
Operation Tool
Practice
  Short Address Assignment
  Data collection
  Advance
Grading Policies
Document Requirements
Deadline

## Slide 3: Device & Software
Device
FT-6251 H.P. ZigBee Sensor Development Board X3
  Sensor Development Board X 1
  Antenna X 1
  A/C Adaptor X 1 ; AA Battery Holder X 1
  UART-to-RS232 Serial Converter X 1
USB to RS-232 Cable X1

## Slide 4: Device & Software
Device

## Slide 5: Device & Software
Software
Windows XP or later
RS232 to USB driver
Code::Blocks
Cygwin : Jennic Bash Shell
Jennic Flash Programmer
Putty

## Slide 6: Preparation
Download Experiments_of_Zigbee.RAR
  http://www.cs.ccu.edu.tw/~cih104m/2017_hw2.zip
Jennic Code::Blocks ：IDE install
  Install JN-SW-4026-SDKwithIDE-1v4.8.msi
  Finish
Install Patch
  Install FT-6200-Patch-ba-1v0.exe
  Install Path “where are your IDE”\jennic

## Slide 7: Operation Tool
Compile Your Program
  Choose build target

## Slide 8: Operation Tool
Compile Your Program
  Press Build → Rebuild
  View build log
    Status 0: success

## Slide 9: Operation Tool
Jennic Flash Programmer
  Burn our data to FT-7251
  Need install USB to RS232 driver
Step1: open Jennic Flash Programmer
Step2: connect FT-7251to your computer
Step3: Press Browse, choose file which you compiled
  Default path: ..\JN5121_Build\Release

## Slide 10: Operation Tool
Jennic Flash Programmer

## Slide 11: Operation Tool
Jennic Flash Programmer
Step4: power off FT-7251
Step5: power on, FT-7251 come into Program mode
  You will find , only one led is bright
Step6: Press Refresh
Notes: 如果MAC address全ff 表機器有問題

## Slide 12: Operation Tool
Jennic Flash Programmer
Step7: press program
Step8: finish
Step9: close flash program and restart FT-7251

## Slide 13: Operation Tool
Output data
  Download putty
  Configure putty

## Slide 14: Practice
Goal
  End device transmits data to coordinator
    Data: Short Address、Temperature、 Humidity 、LQI (between itself and its father node)
  Coordinator output information to computer

## Slide 15: Practice
Short Address Assignment Algorithm
  the nth child router is assigned to address
    Aparent + (n-1) × Cskip(d) + 1
  nth child end device is assigned to address
    Aparent + Rm × Cskip(d) + n

## Slide 16: Practice
Lab 8 – Final.h
  #define MAX_CHILD
    Define max child number
    Set to 1
  #define CSKIP_ADDR
    Define cskip value
    Set to 1

## Slide 17: Practice
Lab 8 -- Final.c
  vHandleNodeAssociation()
    Change sNodeData.sChildData[u16EndDeviceIndex].u16ShortAdr
    sMlmeReqRsp.uParam.sRspAssociate.u16AssocShortAddr
    Child short address
    Set by zigbee address Assignment
  vTickTimerHandler()
    Coordinator do not transmit packet
    Transmit packet to it’s parent
    Use zigbee address Assignment

## Slide 18: Practice
Basic Requirements
  Transfer the data (node A → node B → Coordinator)
  Each nodes Show the receive data information.
  Data ： Data Generated Node 、 Temperature、 Humidity 、LQI (between itself and its father node)、Relay Node

## Slide 19: Practice
A
B
Coordinator

## Slide 20: Practice
Advance Requirements
  Write a program to receive serial port data
    GUI(Presenting data with any patterns except words in your GUI.)
    If any data change large, report an alarm

## Slide 21: Document Requirements
Your document have to include content below
  Cover (group ID, student ID, name)
  An experimental platform and environment
  Code and Explanation about what and how you do
  Final Result
  PDF format
DON'T COPY AND PASTE ALL THE CODE
Compress the PDF and your source code as 組別_HW2.zip
Notes: 上傳至

## Slide 22: Grading Policies
Demo
  地點:創新大樓lab308
  5/9 (二) 10:00-12:00
  5/10(三) 10:00-12:00
Grading
  Basic 65%
  Advance 15%
  Report 20%
BUG：-3 point/ BUG
Delayed：-3 point/ Day

## Slide 23: Uploading to Ecourse
Deadline: 2017/05/10
上傳到Ecourse http://ecourse.elearning.ccu.edu.tw/
格式：“組別_hw2.pdf”
同時繳交一份紙本報告給助教

## Slide 24: Question
TA: 趙柏凱
  Email: a65843@gmail.com